| DSC Power 832 Control Access Codes |
| --- |
| Access codes are used to arm and disarm the system. There are 37 access codes available: 1 master code, 32 regular access codes, 2 duress codes and 2 partition master codes. Ask your installer for more information on using the duress and partition master codes. |
| Only the Master Code can be used to program additional security codes and to change other system features as well as to arm and disarm the security system. The Master Code will be supplied to you by your installer. All keypad entries are made by pressing one key at a time. |
| All access codes can be programmed by following the procedure outlined in "Programming Security Codes" on page 10. |
| NOTE: An access code can be a four or six digit number depending on how your installer has programmed your system. Ask your installer for more information regarding access codes. |
| Arming the System |
| Arming from an LCD Keypad: |
| If the Ready light is ON, the system is ready for arming. If the Ready light is OFF, check to see that all doors and windows are closed and that motion is stopped in areas covered by motion detectors. The system cannot be armed unless the Ready light is ON indicating that all zones are closed and the system is in the Ready State. |
| Enter your access code. As each digit is entered, the keypad sounder will beep. if the access code was entered incorrectly, the keypad buzzer will sound steadily for two seconds. If this occurs, press the [#] key and re-enter your access code. If the correct access code is entered, the keypad sounder will beep quickly and the Armed light will come ON. Exit the premises through the door indicated by your installer as the Exit/Entry door. |
| The panel will provide an exit delay period, indicated by keypad beeps, for you to exit the premises without causing an alarm. At the end of the exit delay period, the Ready light will turn OFF and the system will be armed. The exit delay time can be changed by your installer. |
| When this message appears [Secure System Before Arming] one or more zones are not secured. To secure the system, close all doors and windows and cease all motion in areas covered by motion detectors. Use the arrow < > keys to verify that the system is clear of troubles and that no zones are bypassed unintentionally (see "Viewing Trouble Conditions" on page 12 and "Zone Bypassing" on page 11). |
| If the display is showing [Enter Code to Arm System] the system is in the Ready State and may be fully armed. To arm the system, enter your access code. |
| Once the correct access code has been entered [Exit Delay in Progress] will be showing. The panel will provide an exit delay period, also indicated by keypad beeps, for you to exit the premises without causing an alarm. Exit through the door indicated by your installer as the Exit/Entry door. |
| The message [Enter Code to Disarm System] will be displayed once the exit delay expires and the system is fully armed. |
| If the message [Warning Bypass active] appears, be aware of which zones are bypassed and why (see "Zone Bypassing" on page 11). NOTE: If you arm the system with a zone bypassed or with a trouble present, your security protection is reduced. |
| DSC Power 832 Control Alternate Arming Methods |
| Away Arming Arming the system in the Away mode will have all interior zones and perimeter zones active. If motion is detected in the interior zones, or if one of the perimeter zones is violated, the alarm sequence will begin. To arm in the Away mode, enter your access code and exit the premises through a designated Exit/Entry door. The system will recognize that occupants have left the premises. Once the exit delay expires, the system will be fully armed. |
| Audible Exit Fault In an attempt to reduce false alarms, the Audible Exit Fault is designed to notify you of an improper exit when arming the system in the Away mode. In the event that you fail to exit the premises during the allotted exit delay period, or if you do not securely close the Exit/Entry door, the system will notify you that it was improperly armed in two ways: the keypad will emit one continuous beep and the bell or siren will sound. If this occurs, you must re-enter the premises, enter your access code to disarm the system, and then follow the arming procedure again, making sure to exit the premises in the proper fashion. Your installer will tell you if the Audible Exit Fault has been enabled on your system. |
| Stay Arming The interior zones can be reactivated at any time by entering [*] [1] at any keypad. If you reactivate the interior zones, be sure to only inhabit areas not covered by motion detectors. To access areas protected by motion sensors, you must enter your security code and disarm the system. |
| Arming Without Entry Delay If you wish to arm your system without the entry delay, enter [*] [9] then your access code, The Armed light will flash as a reminder that the system is armed and has no entry delay. An entry through any zone |
| Quick Arm When the Quick Arm feature is enabled, the system may be armed by simply pressing [*] [O] instead of your access code. Please note that pressing [*[O] will only allow you to arm the system; to disarm, you must enter a valid access code. Your installer will inform you if the Quick Arm feature has been enabled on your system. |
| Quick Exit When the Quick Exit feature is enabled, pressing [*] [O] while the system is armed will provide a two minute window for you to exit the premises. During this time, you may only open and close the designated Entry/Exit door once. Once the door is closed, the panel will end the two minute quick exit delay. If the door is opened again, or if the door is not closed after two minutes, or if another zone is opened, the panel will begin the entry delay. Your installer will inform you if the Quick Exit feature has been enabled on your system. |
| DSC Power 832 Control Disarming the System Disarming from the LCD Keypad: Upon entering through a designated Exit/Entry door, the keypad will beep and the entry delay will commence, reminding you to disarm the system. The keypad will display the following message... The correct access code must be entered before the entry delay period expires. If a valid access code is not entered during this time, the system will go into alarm. The entry delay time may be changed by your installer. If an alarm occurred while the system was armed. If a trouble was detected when the panel is disarmed, the Trouble light will turn ON (See "Viewing Trouble Conditions" on page 12 to determine the source of the trouble.) Please note that troubles will not display while the system is in the Alarm Memory Display mode. |
| Entry Active Enter Your Code | Enter your access code. If an error is made in entering the code, press # and enter your code again. When a valid access code is entered, the keypad will stop beeping. If no alarms occurred while the panel was armed, and there are no troubles, the display will read... ____________________________________________ |
| System Disarmed No Alarm Memory | After about five seconds, the system will return to the Ready state and the display will read . Enter Code to Arm System ____________________________________________ |
| View Memory < > Zone of Alarm | If an alarm occurred while the system was armed, this message will be displayed. Use the arrow [< >] keys to view which zones caused the alarm. If a zone is still in alarm, the display will show the following message to indicate that a zone is open. Secure System Before Arming ____________________________________________ |
| Enter Code to Arm System < > | Upon disarming and if a trouble is present, this message will be displayed. Use the arrow [< >] keys to view which troubles are affecting the system (see "Viewing Trouble Conditions" on page 12). ____________________________________________ |
| NOTE: If you return and find that an alarm has occurred while you were away, It is possible that an intruder may still be on the premises. Go to a neighbor's house, and call the local police to investigate. The alarm memory is cleared each lime the panel is armed so that any alarms showing are alarms that occurred only during the last armed period. |
| DSC Power 832 Control Zone Bypassing The zone bypassing function is used when access is needed to part of the protected area while the system is armed. Zones, which are temporarily out of service due to, damaged wiring or contacts may be bypassed to allow system arming until repairs can be made. Bypassed zones will not cause an alarm. Zones cannot be bypassed once the system is armed. Bypassed zones are automatically canceled each time the system is disarmed and must be reapplied before the next arming. |
| NOTE: For security reasons, your installer may program the system to prevent you from bypassing certain zones. Bypassing zones reduces your security protection. If you are bypassing a zone due to damaged wiring or contacts, please call a service technician immediately so that the problem can be resolved and your system returned to proper working order. Do not unintentionally bypass zones when you arm your system. |
| To bypass zones from an LCD keypad: To bypass a zone, the system must be in the Ready state. The display will read... [ Enter Code to Arm System ] Press the [*] key to enter the functions menu. The display will read… [ Press (*) for < > Zone Bypass ] Press (*) key to enter the zone bypassing mode. The display will read... [ Zone Search < > " Zone Name " ] Use the arrow (< >) keys to find the zone to be bypassed and press the [*] key to Select it The display will read... [ Zone Search < > " Zone Name " B ] "B" will appear on the display to show that the zone is bypassed. To un-bypass a Zone, press [*] and the "B" will disappear from the display. A "O" indicates that the zone is open or in need of repair. |
| To exit the bypassing mode and return to the Ready state, press the [#} key. |